BEKARONDO LED

Technical Product Specifications

Table of contents

1.	General Specifications	3

2.	Photometry	3

3.	Mechanics	4

4.	Electrical Characteristics	5

5.	Power Supply	6

6.	Environment	6

# General Specifications

| Product Description | The luminaire consists of a pressed metal ceiling trim, reflector, ceiling brackets and reinforced luminaire frame. Available in Eco or High-efficiency version. Designed to operate LED light sources of up to 23W in an ambient temperature environment of up to 35˚C, without reducing the useful lifetime of 50 000 hours (Eco) or 60 000 hours (High-efficiency), at a lumen depreciation of not more than 30% (L70). The easy-fixing ceiling brackets are made of spring steel to ensure rigid and positive mounting in the ceiling, eliminating any sagging of the luminaire. Effective high-power LED, 3000K or 4000K, at a colour rendering index ≥80. The 99.9% pure aluminium reflector is made from pressed grade 1050 aluminium alloy |
| --- | --- |
| Main applications | Hotel and catering trade Schools and lecture rooms Retail Service areas The arts Public access and circulation areas |
| Recommended mounting height |  |

# Photometry

| Light source | LED |
| --- | --- |
| LED | Mid Power LED’s |
| Light color | Neutral White (4000K) / Warm White (3000K) |
| Color rendering (Ra) | >80 |
| Lumen package 9W 9W 10W 10W 16W 17W 19W 19W 23W 23W | 1250lm - Neutral White (4000K) 1250lm - Warm White (3000K) 1000lm - Neutral White (4000K) 1000lm - Warm White (3000K) 2240lm - Neutral White (4000K) 2270lm - Warm White (3000K) 2000lm - Neutral White (4000K) 2000lm - Warm White (3000K) 3390lm - Neutral White (4000K) 3220lm - Warm White (3000K) |
| Optics |  |
| Photometry: |  |

| Overview |
| --- |
| Luminaire |  | Warm White (3000K) | Neutral White (4000K) |
| BEKARONDO LED Eco 10W | Nominal Flux (lm)* | 1000 | 1000 |
|  | Power Consumption (W) | 10 | 10 |
| BEKARONDO LED Eco 19W | Nominal Flux (lm)* | 2000 | 2000 |
|  | Power Consumption (W) | 19 | 19 |
| BEKARONDO LED HE 9W | Nominal Flux (lm)* | 1250 | 1250 |
|  | Power Consumption (W) | 9 | 9 |
| BEKARONDO LED HE 16W/17W | Nominal Flux (lm)* | 2240 | 2270 |
|  | Power Consumption (W) | 16 | 17 |
| BEKARONDO LED HE 23W | Nominal Flux (lm)* | 3220 | 3390 |
|  | Power Consumption (W) | 23 | 23 |

(*) The type of LED used is subject to change due to the ongoing rapid progress taking place in LED technology

(**) LED Current

# Mechanics

| Electronic control Gear | Constant Current Driver |
| --- | --- |
| Materials and finishing | Housing – Aluminium |
| Coating | Trim ring: Standard colour: Chrome or White (RAL 9016) RAL colours on request |
| Installation | Ceiling mount |
| Fixing | 2 x Steel Springs |
| Dimensions (LxWxH) | Ø232 x 123.5 (1000lm) Ø232 x 154 (2000lm) |
| Weight (with gear) | 0.9 – 1.2kg |
| Access | Yes |

# Electrical Characteristics

| Line Voltage | 230VAC |
| --- | --- |
| Mains voltage Tolerance (AC) | 198-265V |
| Line frequency | 50Hz |
| Electrical Safety Class (IEC) | Class I |
| Surge protection | No |
| Lighting control | Optional - DALI - 1-10V - Push-dim - Phase-cut |

# Power Supply

| Power Factor | ≥0.9 |
| --- | --- |
| Removable | Yes |
| Thermal Safety | Yes |

# Environment

| Storage temperature | -40< T < 60 |
| --- | --- |
| Enclosure Tightness |  |
| Enclosure Mechanical Withstand Impact |  |
| Enclosure Mechanical Withstand Vibrations | Modified IEC 60068-2-6 |

| Updated by | Approved by | Document Revision / Date |
| --- | --- | --- |
| Nadja Smith | Pieter van Aardt | 23/03/2021 |

- For specific Tq, Ta and life time data, contact BEKA Schréder